## Slide 1: DETERMINISM & Memory allocations in labview
Mark Randel (CLA)

## Slide 2: Mark Randel (CLA)
Senior Software Engineer - JKI
Over 30 years engineering
Started with LabVIEW 2.0 in 1990
Industries: Defense & Aerospace, Medical, Manufacturing, Robotics
  Spent 6+ years at SpaceX (McGregor) designing and supporting Test Software infrastructure

## Slide 3: #OurGiantsAreFemale
Gwynne Shotwell
President & COO SpaceX
Earned BS and MS degrees in Mechanical Engineering and Applied Mathematics from Northwestern University
Worked at The Aerospace Corporation for 10 years, becoming Chief Engineer of spacecraft program
Joined SpaceX in 2002 as Vice President of Business Development
Promoted to President and COO in 2008
Led development of Falcon rockets and Dragon spacecraft
Pioneered reusable rocket technology
Named in Time’s 100 most influential people (2020)

## Slide 4: Determinism defined
Not the philosophical definition

## Slide 5: Determinism in LabVIEW
Definition: A deterministic system is one where future states are predictably determined by current conditions, with no randomness involved.
Challenge in Windows: Windows introduces potential non-determinism due to background processes and system management.
Real-Time Operating Systems (RTOS): Even RTOS can introduce non-determinism if forced to reallocate memory.

## Slide 6: Ideal vs. Real World
Sequence
Scale & Math
Read (DAQ)
Write (DAQ)
Network Write
System Rate: 200Hz
(5mSec Period)
Chart: Control System frames (Actual)
Chart: Control System frames (Ideal)

## Slide 7: Memory Allocations in LabVIEW
Definition: Assignment of physical or virtual memory for program use
LabVIEW Compiler Behavior:
  Predicts and reserves memory at start time
  Dynamic allocations occur during runtime
Causes of Runtime Allocations:
  Changes in array size
  Changes in string length
Impact on Determinism:
  Each allocation/resize requires Memory Manager adjustment
  Adjustment time is unpredictable, introducing non-determinism

## Slide 8: Desktop Execution Trace Toolkit (DETT) – For Further Study
Note: This presentation is not a DETT tutorial. For in-depth learning, refer to LabVIEW documentation.
Relevance to Memory Allocations:
  Tracks real-time memory allocation
  Helps identify run-time allocations
There is much more to DETT than is covered in this presentation. (Possibly a future presentation?)

## Slide 9: Basic Example

## Slide 10: Applied to real world problems
Enough with the setup. Let’s see the goods.

## Slide 11: Async Data Transmit to Network
A control program is required to send ALL of its data out over the network
The data size can vary between a couple hundred to thousands of channels
The network protocol can only support a limited number of channels per packet
Implement an asynchronous daemon to serialize data for transmission
Data
[variable]
Full Packet
Full Packet
Full Packet
Full Packet
Full Packet
Partial

## Slide 12: Test Setup: Isolate the snippet

## Slide 13: Test Setup: Memory Allocations
Data Size: 12,000 channels
Max Packet: 5,000
Resulting in:
Packet Size
[5000]
Packet Size
[5000]
[2000]

## Slide 14: Basic Approach
DETT results with Test 1 setup
Data
[12,000]
Packet Size
[5000]
Packet Size
[5000]
[2000]

## Slide 15: IPE’s & Pre-allocated Packet
DETT results with Test 1 setup
Data[1]
(5000)
Data[2]
(5000)
Data[3] (2000)
Packet Size
[5000]
Packet Size
[5000]
[2000]

## Slide 16: Add Packet Type Case
DETT results with Test 1 setup
Data[1]
(5000)
Data[2]
(5000)
Data[3] (2000)
Packet Size
[5000]
Packet Size
[5000]
[2000]
Full Set
Last Set

## Slide 17: Packet Type Case (no IPE)
DETT results with Test 1 setup
Data[1]
(5000)
Data[2]
(5000)
Data[3] (2000)
Packet Size
[5000]
Packet Size
[5000]
[2000]
Full Set
Last Set

## Slide 18: Test Setup: Performance
Data Size: 43,623 channels
Max Packet: 5,000
Resulting in:
  Packets 1-8: 5,000 chans
  Packet 9: 3,632 chans

## Slide 19: Test 2: Performance
Parameters | Basic | Preallocated w/ IPE’s | Preallocated w/ IPE’s & Case | Preallocated w/ Case (no IPE’s)
Mean Time (μS) | 220.3 | 166.7 | 156.1 | 158.5
StdDev (μS) | 16.5 | 10.7 | 8.3 | 9.6
Variance (nS2) | 0.272 | 0.115 | 0.068 | 0.091
Max Time (μS) | 460.8 | 298.7 | 260.8 | 302.7
Min Time (μS) | 203.7 | 155.3 | 147.9 | 148
Iterations: 10,000
Data Size: 43,623
Max Packet Size: 5,000

## Slide 20: Lab Lessons Learned
Performance tests can vary. To minimize variation:
  Do NOT leave DETT running
  Close all sub-VI’s (front panel updates == unpredictable timing)
  Don’t use debugging or probes
  Close out of all other programs in Windows
  Run all compared tests on the same computer
  … Don’t rely strictly on performance tests
System level performance testing is the final verdict

## Slide 21: Summary
Memory allocations have a direct impact on determinism
In-Place Element’s should be used with care and thought
Attempting to predict the LabVIEW compiler is complicated and changes with each new release.
When in doubt, Lab it out

## Slide 22: "Before you use a sledgehammer, make sure it's not a nail."
- Unknown

## Slide 23: Thank you
Mark Randel
mark.randel@jki.net

## Slide 25: Post-Credit teaser!
Coming Soon

## Slide 26: Extra slides
Data Plots

## Slide 27: Simple Data Encoder

## Slide 28: Preallocated Data Encoder

## Slide 29: Add Packet Type Case

## Slide 30: Simple Packet Type Case (no IPE)